## Batteries

FOR SMART-CASE XS (A 90 64 107 / 109 / 209)

Available in photo shops and consumer markets worldwide.

Typical batteries for cameras. Large quantities direct from well-known battery manufacturers.

1 round cell 12 volts / 33 mAh, Ø 10.3 mm, length: 28.5 mm. This battery has no standardised designation!  Product identification of some manufacturers: VARTA V 23 GA, UCAR A23, DURACELL MN21, DURACELL VR22, DURACELL MS21, ALCATEL 32A12V. Fixing and contacts by means of metal clips, straps or strips soldered onto the PCB. Clips/straps/strips commercially available (e.g. Ettinger) or self-made.

Standard button cells also fit. Suitable button cell holders for soldering on are available from well-known electronic component dealers (e.g. Ettinger).

Note: The 1.5 V round cell (N), Ø 12 mm x 30.2 mm long, which is quite commonly used, cannot be used here as it is too large. According to the manufacturer, this model is gradually being discontinued.

No responsibility is taken for the correctness of this information.

Odenwälder Kunststoffwerke

Gehäusesysteme GmbH

Friedrich-List-Str. 3

74722 Buchen/Germany

www.okw.com